## Slide 1: WIFI based indoor localization using decision tree algorithm
Mrinmoy Sarkar
PhD student, ECE department
11/06/2018
Short Presentation

## Slide 2: Problem Statement
Why do we need such a system?
  Asset tracking
  Inventory management
  Autonomous robot navigation
How can we localize objects or things inside a building?

## Slide 3: Existing Solutions
Global Positioning System(GPS)
  Does not work well indoor
Triangulation
  Uses the geometric properties of triangles to estimate the target location
  Instead of measuring the distance directly using received signal strengths (RSS), time of arrival (TOA) or time difference of arrival (TDOA) is usually measured
  Suffers from multipath fading and shadowing
Proximity
  Proximity algorithms provide symbolic relative location information
  Relies upon a dense grid of antennas, each having a well-known position
Scene Analysis
  Uses location fingerprint
  Location fingerprinting refers to techniques that match the fingerprint of some characteristic of a signal that is location dependent

## Slide 4: Proposed method
Benefits of this method:
WIFI is readily available in any modern building
Don't need any new infrastructure
Cost effective
Don’t need any model of communication channel
The prediction model can be updated from time to time with new data
Decision tree based indoor localization using RSS signal from WIFI receiver. The technique lies in scene analysis.
There are two stages for this technique: offline stage and online stage (or run-time stage).
During the offline stage, a site survey is performed in an environment. The location coordinates/labels and respective signal strengths from nearby base stations/measuring units are collected.
During the online stage, a location positioning technique uses the currently observed signal strengths and previously collected information to figure out an estimated location.

## Slide 5: Data and expected results
Expected results:
Accuracy of the model
Mean square error(MSE) of the trained model
650 samples of data with 127 features and 2D(x, y) location information associated with the 127 features. 127 features are RSSI level for each different WAPs retrieved during the campaign.

## Slide 6: Plan
Literature Review |  |  |  |  |  |  |  |  |  | 
Data Preprocessing |  |  |  |  |  |  |  |  |  | 
Coding of simple model |  |  |  |  |  |  |  |  |  | 
Development of main codebase |  |  |  |  |  |  |  |  |  | 
Fine Tuning Of the model |  |  |  |  |  |  |  |  |  | 
Documentation of the result |  |  |  |  |  |  |  |  |  | 
Preparing the final report |  |  |  |  |  |  |  |  |  | 
 | W1 | W2 | W3 | W3 | W4 | W4 | W5 | W5 | W6 | W7
N.B.: W stands for Week, Purple = past weeks, Green = present week, Blue = future weeks

## Slide 7: References
[1] Barsocchi, P., Crivello, A., La Rosa, D., & Palumbo, F. (2016, October). A multisource and multivariate dataset for indoor localization methods based on WLAN and geo-magnetic field fingerprinting. In Indoor Positioning and Indoor Navigation (IPIN), 2016 International Conference on (pp. 1-8). IEEE.
[2] Liu, H., Darabi, H., Banerjee, P., & Liu, J. (2007). Survey of wireless indoor positioning techniques and systems. IEEE Transactions on Systems, Man, and Cybernetics, Part C (Applications and Reviews), 37(6), 1067-1080.

## Slide 8: Thank you